## Slide 1: A Systematic Approach for Register File Design in FPGAs
Hasan Erdem Yantır
Computer Engineering, Bogazici University
P.K. 2 TR-34342 Bebek, Istanbul, TURKEY
Phone: +90 212 359 7780, Fax: +90 212 287 2461
hasanerdem.yantir@boun.edu.tr
Computer Architecture & Systems Laboratory
http://www.cmpe.boun.edu.tr/caslab

## Slide 2: Introduction
Technology trend shifts towards to the parallel & heterogeneous platforms
Such platforms require to process more data per unit time so need multi-port RFs
2-way Superscalar Processor
N-issue VLIW Processor
Notes: For example a 4-issue VLIW requires at least 8 read and 4 write ports. As the issue width increases # of RW ports have to increase accordingly.
A single-issue processor typically requires a register file with two read ports and one write port. A superscalar processor, on the other hand, requires additional ports to support more instructions per cycle.

## Slide 3: Introduction
FPGAs are the best candidates for these type of platforms hence each part can be configured to perform a different task that is best suited for.
Unfortunately, FPGA lacks of multi-ported RFs.
  Ex. No ILP in MicroBlaze, Picoblaze, Nios II
So multi-ported Register File (RF) is required for FPGAs
Notes: For example a 4-issue VLIW requires at least 8 read and 4 write ports. As the issue width increases # of RW ports have to increase accordingly.
A single-issue processor typically requires a register file with two read ports and one write port. A superscalar processor, on the other hand, requires additional ports to support more instructions per cycle.

## Slide 4: Ideal Multi-Ported RF
Ideal multi-ported RF (multiple read & write)
  No contention
  No serialization
In real word,
  Multiplexer delays
  Area overhead

## Slide 5: Storage Units in FPGAs
Two storage units in FPGAs
  1. Slices (Distributed)
    FFs, LUTs and multiplexers inside the slices
  2. Block RAM (Bulked)
    Implemented directly in dedicated hardware
    Two ports which can function either as read or write
    Fixed storage capacity and number of ports
    ex. In Virtex-5 148 × 36Kbits
If size > 4 Kb, BRAM is better
Slice
Block RAM
Notes: In general, BRAMs use less area and run at a higher frequency (550 Mhz) than ones created from slices, but do so at the expense of having a fixed storage capacity and number of ports.
On the right side of the slide, you can see the corresponding figures.
Using BRAM is better than the slice based RF.

## Slide 6: Conventional Approaches Distributed Replication Banking Multi-pumping
FFs inside the slices
n-read + m-write ports with D location
Input: D x m-to-one multiplexers
Output: n x D-to-one multiplexers
Flexible but slow
Area inefficiency & limiting
S: Storage
Notes: However, this design is not scalable at all because the combinational and wiring delays of slices dominate as the number of ports increases.
This architecture is flexible but slow.

## Slide 7: Conventional Approaches (Cont'd) Distributed Replication Banking Multi-pumping
Using Block RAMs
Increase # of read ports by replicating data
XST supports to automatic replacement
No more than one write port

## Slide 8: Conventional Approaches (Cont'd) Distributed Replication Banking Multi-pumping
Divides memory locations among multiple BRAMs
Each additional bank =>1R&1W
Fragmentation

## Slide 9: Conventional Approaches (Cont'd) Distributed Replication Banking Multi-pumping
Internal ports run at faster (multiple) freqeuncy than the external ports so illustrates one resource as if there exists multiple replications of this resource.
Requires multiplexers and registers to temprorary hold data & addresses
Increasing port number => decrease in external operating frequency
Multi-pumping factor;
Notes: Multi-pumping is setting the RF internal operating frequency by the times of system external operating frequency. So, multiple read and write operations in memory can be carried out in a time-shared manner. The ratio between RF internal operating frequency and system external operating frequency is defined as multi-pumping factor (MPuF).
Clock internal is used by BRAM while clock external is used by other sequential component of the circuit.
For example, if your MPuF=5 and BRAM runs at 500 Mhz, then external system that uses BRAM should run at most 100 Mhz.
This essentially involves a data access time (halved) versus functionality (doubled) trade-off.

## Slide 10: Problems & Our Solution
Problems
  Distributed RF not scalable
  Banking, replication not result in a real multi-port RF
  In general, dedicated logic part runs faster than reconfigurable part of the FPGA: ex. A mid-level CPU runs @ 125 MHz although BRAM can run up to 550 MHz in Virtex-5 underutilization of BRAMs
  Using multiplexer based MPu causes performance degradation
Solution: Emulated Register File [ERF]
  Combination of replication, banking and efficient shift-register multi-pumping
Notes: The conventional multi-pumping approach is based on the utilizing multiplexers and demultiplexers at the inputs and outputs. Yet, this approach is also not scalable because of the increased combinational delay in multiplexers and demultiplexers when the number of read- and write ports increases
The solution that we have proposed... [FOCUS]

## Slide 11: Our Solution: Base RF + Multi-Pumping
First, a base register file is implemented by replication and banking
Then, shift register based multi-pumping method is applied

## Slide 12: Our Solution: Base RF + Multi-Pumping (Replication & Banking) [Sagmir et al.]
BRAMs connected to each other by replication and banking
In a bank, all BRAMs contain the same data
Address space shared between the banks
  All write operations should be mutually exclusive wrt associated bank
  In order to handle this problem, registers trying to access the same bank at the same time are renamed and directed to different banks by compiler. [Anjam et al.]
# of read ports can be increased by adding extra BRAMs to each bank
# of write ports can be increased by adding extra banks

## Slide 13: Our Solution: Base RF + Multi-Pumping (Replication & Banking)
Example 2R&3W RF
Notes: Figure illustrates how six such BRAMs can be used to implement 512×64-bit RF with 2R&3W ports.
In the example, there are three write ports so there should be three banks. The first bank holds the data between 0 and 127 and the second bank holds 128-255 and the third bank 256-512 However, though each BRAM has 512 locations, only the first 128 locations are used in the first and second banks, and 256 locations are used in the third bank. For the third bank, the range between 0-255 correspond to the range between 256-512 in the designed MPo-RF.
During a write operation, the value is written to the corresponding register bank. However it is not possible to realize more than one write operations to the same bank at the same time. All write operations should be mutually exclusive with respect to the associated bank.

## Slide 14: Our Solution: Base RF + Multi-Pumping (Overall Architecture)
Banking and replication of BRAMs with efficient shift register based multi-pumping (SR-MPu) approach.

## Slide 15: Our Solution: Base RF + Multi-Pumping (Shift Registers)
PISO (Parallel Input Serial Output) Shift Register
SIPO (Single Input Parallel Output) Shift Register
Notes: As all of you have already known very well …

## Slide 16: RF Operation
0x02
0x05
0x00
0x07
0x09
0x04
0x01
0x08
0x03
1478
2589
3698
1598
1236
2568
7541
1154
5987
1598
1236
2568
7541
1154
5987
Read Ports
Write Ports
Notes: [FOCUS]

## Slide 17: Methodology
Automatic generation and implementation of RF designs
  Varying # of ports, width, depth, MP factor, MP Type, RF type
  All external signals are registered and IO delays are omitted (internal design)
  Timing constraints forced until fails to find best results
Speed [MHz], Area [# of Occupied Slices]
Energy [nJ] (power × delay)
  XPA used with %100 activity ratio on wires.
Target FPGA: Xilinx Virtex-5
  148 BRAMs ( 2×18Kb or 1×36Kb)

## Slide 18: Experimental Results SR-MPu vs Mux-MPu Performance
3R&2W Performance Results
Internal speed remains constant nearly
Internal Frequency
External Frequency

## Slide 19: Experimental Results SR-MPu vs Mux-MPu Area
3R&2W Area Results
SR-MPu occupies fewer resources
Area

## Slide 20: Experimental Results SR-MPu vs Mux-MPu
4R&2W and 8R&4W Results
Area
Internal Frequency
External Frequency

## Slide 21: Experimental Results RF Evaluation
4R&2W 512 location and MPuF=2 RF with varying width
Chart: Maximum Internal Frequency
| 32 | 64 | 128 | 256
SR-MPu | 408.33 | 390.016 | 393.701 | 335.909
Mux-MPu | 344.116 | 330.36 | 329.489 | 299.401
Chart: Area
| 32 | 64 | 128 | 256
SR-MPu | 104 | 167 | 297 | 552
Mux-MPu | 196 | 318 | 617 | 1358

## Slide 22: Experimental Results RF Evaluation
Chart: Maximum External Frequency
| Distributed (12R&6W) | MPo (12R&6W) | MPo (6R&3W) MPuF=2 | MPo (4R&2W) MPuF=3 | MPo (2R&1W) MPuF=6
SR-MPu | 187.793 | 302.115 | 193.125 | 136.277 | 71.654
Mux-MPu | 187.793 | 302.115 | 160.411 | 114.982 | 62.941
Different ways to implement 12R&6W RF

## Slide 23: Experimental Results RF Evaluation
Different ways to implement 12R&6W RF
Chart: Area [Logarithmic Scale]
| Distributed (12R&6W) | MPo (12R&6W) | MPo (6R&3W) MPuF=2 | MPo (4R&2W) MPuF=3 | MPo (2R&1W) MPuF=6
SR-MPu | 5364 | 312 | 136 | 155 | 165
Mux-MPu | 5364 | 312 | 257 | 213 | 176
Notes: In this logarithmic chart ….

## Slide 24: Experimental Results RF Evaluation
Different ways to implement 12R&6W RF
Chart: Power-Delay Product
| Distributed (12R&6W) | MPo (12R&6W) | MPo (6R&3W) MPuF=2 | MPo (4R&2W) MPuF=3 | MPo (2R&1W) MPuF=6
SR-MPu | 6.055 | 3.267 | 0.753 | 0.367 | 0.16
Mux-MPu | 6.055 | 3.267 | 0.823 | 0.444 | 0.214

## Slide 25: Experimental Results RF Scalability
32R&24W, 64-Bit, 512 location
  No way to implement as distributed or pure multi-port
Chart: Maximum External Frequency
| MPo(8R&6W) MPuF=4 | MPo(4R&3W) MPuF=8
SR-MPu | 75.301 | 47.099
Mux-MPu | 56.117 | 33.512
Chart: Power-Delay Product
| MPo(8R&6W) MPuF=4 | MPo(4R&3W) MPuF=8
SR-MPu | 2.643 | 1.101
Mux-MPu | 3.58 | 1.24

## Slide 26: ERF Conclusion
In SR-MPoMPu RF, internal operating freqency is independent from MPuF
SR Method results in faster RF and occupies fewer resources.
SR-MPoMPu RF consumes up to 25% less energy than other methods
Notes: In this paper, we focus on efficient implementations of multi-ported RFs with exploting a new multi-pumping approach called shift register based multi-pumping (SR-MPu).

## Slide 27: ERF Modelling for HLS Tools
HLS tools require modeled libraries for each primitive
Motivation,
  Internal operating frequecy remains constant with increasing MPuF. For 2R&1W 32-bitx512 RF,
  Delay and area models are in coherence with R# and W#
In progress

## Slide 28: HLS 32-bit x 512 RF Model @ MPuF 2

## Slide 29: HLS Example
A 4 pairwise 32-bit multiplication circuit @ 100 Mhz
Requires 8R&4W 32-bit RF
For 2R&1W RF,
  f(2,1) = 419,946 MHz
  2R&1W RF with MPuF =4
  419,946 / 4 > 100
  Emulated 8R&4W RF with internal frequency 400 Mhz, external frequenc 100MHz.

## Slide 30: HLS Conclusion
ERF can be modeled easily hence internal frequency independent from MPuF
These models can be used in HLS tools
In Progress (Future Work)

## Slide 31: Heterogeneous Register File
In single-FPGA heterogeneous computing, DSP processors, hardcore/softcore processors, custom logical circuits, VLIW processors may be together. [Rusten]
Each processing element has its own
  clock domain (running frequency)
  number of read/write ports
  data width
  address space
  endianness (big-endian or little-endian).

## Slide 32: Heterogeneous Register File Single-FPGA Heterogeneous System

## Slide 33: Heterogeneous Register File Architecture – Base HRF
Each processing element has its own address space for write
PEs can reach entire address space to read
Global Address Space vs Local Address Space
Data widths may be different for each bank
Notes: Global address space vs local address space

## Slide 34: Heterogeneous Register File Endiannes, Sign Pass, Output Data Width
Endianness;
Data Sign;
Output Data Width; the largest data width of PEs
Notes: Existing work, more refences

## Slide 35: Heterogeneous Register File SR-MPu
For each PE, different MPuF is applied to corresponding ports

## Slide 36: Heterogeneous Register File Experimentation
4 different heterogeneous architectures

## Slide 37: Heterogeneous Register File Area Results
When complexity increases, there is no way to implement RFs except HRF
Chart: Area in LUT-FF Pairs [Logarihmic Scale]
| System 0 | System 1 | System 2 | System 3
HRF | 146 | 401 | 1058 | 2247
MPo | 132 | 292 | 1670 | 0
Distributed | 10910 | 21397 | 0 | 0
Chart: Area in BRAMs [Logarithmic Scale]
| System 0 | System 1 | System 2 | System 3
HRF | 2 | 3 | 15 | 56
MPo | 16 | 36 | 156 | 0
Distributed | 0 | 0 | 0 | 0

## Slide 38: Heterogeneous Register File Frequency & PxD Results
Chart: Max Internal Frequency
| System 0 | System 1 | System 2 | System 3
HRF | 373.413 | 359.195 | 334.56 | 292.398
MPo | 388.199 | 339.905 | 238.949 | 0
Distributed | 236.686 | 148.368 | 0 | 0
Chart: Power Delay Product
| System 0 | System 1 | System 2 | System 3
HRF | 3.198 | 3.402 | 3.99 | 5.893
MPo | 3.46 | 4.463 | 9.207 | 0
Distributed | 7.728 | 18.299 | 0 | 0
In System 0, HRF is slower because system. However in complex systems, HRF is better.
HRF always consume less energy

## Slide 39: Conclusion
Both ERF and HRF outperform the conventional RF implementations in FPGAs and provides significant power and area reductions
HRF is the first study on FPGA-based heterogeneous RF in the literature

## Slide 40: Questions? Comments? Thank you for your attention…
hasanerdem.yantir@boun.edu.tr
Computer Architecture & Systems Laboratory
http://www.cmpe.boun.edu.tr/caslab

## Slide 41: Publications
Hasan Erdem Yantır, Salih Bayar and Arda Yurdakul, "Efficient Implementations of Multi-pumped Multi-port Register Files in FPGAs" 16th EUROMICRO Conference on Digital System Design (DSD), September 4 – 6, 2013, Santander, Spain.
Hasan Erdem Yantır and Arda Yurdakul, "A Register File Architecture for Single-FPGA Heterogeneous Computing Systems" 51st Annual Design Automation Conference (DAC'14) (Submitted)
Hasan Erdem Yantır and Arda Yurdakul, "An Efficient Heterogeneous Register File Implementation for FPGAs" 21st Reconfigurable Architectures Workshop (RAW‘14) (Submitted)

## Slide 42: References
[Sagmir et al.] M. A. R. Saghir and R. Naous, “A configurable multi-ported register file architecture for soft processor cores,” in Proceedings of the 3rd international conference on Reconfigurable computing: architectures, tools and applications, ser. ARC’07. Berlin, Heidelberg: SpringerVerlag, 2007, pp. 14–25. [Online]. Available: http://dl.acm.org/citation.cfm?id=1764631.1764634
  [Anjam et al.] F. Anjam, S. Wong, and F. Nadeem, “A multiported register file with register renaming for configurable softcore vliw processors,” in fieldProgrammable Technology (FPT), 2010 International Conference on, Dec., pp. 403–408.
  [Rusten] Leif Tore Rusten, “ Implementing a Heterogeneous Multi-Core Prototype in an FPGA, “ MSc Thesis 2012 Norwegian University of Science and Technology